Southwestern Industries, Inc.
TRAK K2 EMX Knee Mill 
with the ProtoTRAK EMX CNC

# TRAK K2 EMX Machine Specifications

- ProtoTRAK Control model -EMX

- Table Size-50" X 10"

- Table Travel -31"

- Saddle Travel-15.5"

- Knee Travel:-13.5"

- Ram Travel-21"

- Maximum Quill Travel-5"

- Quill Diameter-3.375"

- Spindle Taper-R8

- Spindle Speed  Range -70-4200 RPM

- Head Tilt-45° forward and back, 90° left and right

- Quill feeds per rev-0.0015”, 0.003”, 0.006”

- Spindle Motor- vari-speed-3 HP

- Power Requirement Control-110V; 1P; 8A

- Power Requirements Machine -220/440V; 3P; 8.5/4.3A

- Maximum Weight on Table-850 lbs

- Machine Weight:-2820 lbs

- Machine dims: l x w x h-71" x 59" x 87"

- Maximum rapid feed-100 IPM

- Way surface type-Dovetail: X, Y, Z

- Precision 7207 CP4 Spindle bearings

- Chrome hardened and ground quill

- Slide ways are Turcite coated

- Wide way surfaces are hardened and ground

# ProtoTRAK EMX CNC

# Control Hardware Specifications

- Two-axis CNC, three-axis DRO

- Digital Servo Amplifiers – custom designed for ProtoTRAK operation

- D.C. Servo Motors – rated at 280 in-oz. Continuous torque are twice that required

- Precision Ground Ball Screws – in the table and saddle

- Modular Design – simplifies service and maximized uptime

- 115V/60HZ/15 amps

- Feedrate Override of programmed feedrate and rapid

- Polycarbonate Sealed Membrane Keypad and Gasket Sealed Control

- Enclosures to lock out contamination

- 7.4” LCD with adjustable contrast

- Floppy Disk Storage for part programs

- Rugged Industrial PC

# Software

- Part geometry programming – the tool path is generated for you automatically

- Diameter Cutter Compensation – allows programming of the part rather than the center of the tool path

- Circular interpolation – makes arcs and any size hole easy to do with standard tools

- Linear Interpolation – to machine lines at any angle

- Conrad – provides automatic corner radius programming with one data input

- Incremental and Absolute – programming can even be mixed within an event

- Error Messages – to identify programming mistakes

- Fault Messages – for system self-diagnostics

- Program Downloading – from offline CAD/CAM systems via a modified FANUC 6 post-processor

- Teach – to program manual position and mill moves

- Parts Graphics display

- Look – a single button press to view graphics during programming

- Math Help – for finding points in a prompted format with graphical representation of prompts

- Machine Tool Error Compensation and Backlash Compensation custom set on mill after installation

- Selectable Inch/mm measurement readout

- Jog of X and Y from 1 to 100 inches per minute

- Continue Mill to eliminate repetitive data inputs while programming

### Programmed Canned Cycles

- Posn/Drill – single point

- Bolt Hole – series of points evenly spaced around a circle

- Mill – straight line in any direction

- Arc – any portion of a circle

- Pocket – a rectangle or circle and all the material inside, includes finish cut

- Frame – a perimeter of a rectangle or circle, includes finish cut

- Repeat – of programmed events with or without offset

# Service

- The SWI Customer Service Group provides after-sale support over the telephone via a toll-free service number - (800) 367-3165.

- Machine design makes self-service easy for when the customer is able to resolve the problem.

- Express Exchange program in which nearly all electronic and mechanical sub-assemblies are in stock.  In response to a problem, any parts you need may be shipped to arrive the next day.

# Available option / accessories

- Remote Stop/Go Switch

- Power drawbar

- Halogen worklamp

- Chip pan

- Knee power feed

- Coolant pump

- Table guard

- Vise

- USB memory stick

- Auto lube pump

- Spray coolant