Southwestern Industries, Inc.
TRAK K3 EMX Knee Mill 
with the ProtoTRAK EMX CNC

TRAK K3 EMX Machine Specifications

- Table Size –50” X 10”

- T-Slots – 5/8” x 3 x 2 ½”

- Table Travel – 32”

- Saddle Travel – 16”

- Knee Travel – 16”

- Ram Travel – 24”

- Maximum Quill Travel – 5”

- Quill Diameter – 3 3/8”

- Spindle Taper – R8

- Spindle Speed Range – 60-4200 RPM

- Head Tilt – 45 deg. forward, 45 deg. back, 90 deg. left, 90 deg. right

- Spindle Motor – 3 HP

- Power Requirement Control – 110V; 1P; 10A

- Power Requirement Machine – 220/440V; 3P; 8.5/4.25A

- Maximum Weight on Table – 850 lbs.

- Machine Weight – 2816 lbs.

- Machine dims l,w,h, - 71” x 59” x 84”

- Maximum rapid feed – 100 IPM

- Way surface type – Dovetail X, Z Square Y

- Precision 7207 CP4 spindle bearings

- Chrome hardened and ground quill

- Meehanite castings

- Slide ways are Turcite coated

- Wide way surfaces are hardened and ground

ProtoTRAK EMX CNC

Control Hardware Specifications

- Two-axis CNC, three-axis DRO

- Digital Servo Amplifiers – custom designed for ProtoTRAK operation

- D.C. Servo Motors – rated at 280 in-oz. Continuous torque are twice that required

- Precision Ground Ball Screws – in the table and saddle

- Modular Design – simplifies service and maximized uptime

- 115V/60HZ/15 amps

- Feedrate Override of programmed feedrate and rapid

- Polycarbonate Sealed Membrane Keypad and Gasket Sealed Control

- Enclosures to lock out contamination

- 7.4” LCD with adjustable contrast

- Floppy Disk Storage for part programs

- Rugged Industrial PC

Software

- Part geometry programming – the tool path is generated for you automatically

- Diameter Cutter Compensation – allows programming of the part rather than the center of the tool path

- Circular interpolation – makes arcs and any size hole easy to do with standard tools

- Linear Interpolation – to machine lines at any angle

- Conrad – provides automatic corner radius programming with one data input

- Incremental and Absolute – programming can even be mixed within an event

- Error Messages – to identify programming mistakes

- Fault Messages – for system self-diagnostics

- Program Downloading – from offline CAD/CAM systems via a modified FANUC 6 post-processor

- Teach – to program manual position and mill moves

- Parts Graphics display

- Look – a single button press to view graphics during programming

- Math Help – for finding points in a prompted format with graphical representation of prompts

- Machine Tool Error Compensation and Backlash Compensation custom set on mill after installation

- Selectable Inch/mm measurement readout

- Jog of X and Y from 1 to 100 inches per minute

- Continue Mill to eliminate repetitive data inputs while programming

Programmed Canned Cycles

- Posn/Drill – single point

- Bolt Hole – series of points evenly spaced around a circle

- Mill – straight line in any direction

- Arc – any portion of a circle

- Pocket – a rectangle or circle and all the material inside, includes finish cut

- Frame – a perimeter of a rectangle or circle, includes finish cut

- Repeat – of programmed events with or without offset

# Service

- The SWI Customer Service Group provides after-sale support over the telephone via a toll-free

- service number - (800) 367-3165.

- Machine design makes self-service easy for when the customer is able to resolve the problem.

- Express Exchange program in which nearly all electronic and mechanical sub-assemblies are in stock.

- In response to a problem, any parts you need may be shipped to arrive the next day.

Available Options/Accessories

- Off-line Programming for running the ProtoTRAK software on the PC

- Remote Stop/Go (RSG) switch

- Power Drawbar

- Halogen Worklamp

- Chip Pan

- Riser Block

- Knee Power Feed

- Coolant Pump