Southwestern Industries, Inc.
TRAK DPM FHM7 Bed Mill

with the ProtoTRAK SMX CNC

# Machine specifications

- Table size – 76” x 14”

- T-slots (number x width x pitch) – 3 x 63” x 2.48”

- Travel (X, Y, Z axis) – 60” x 23” x 20.5”

- Quill diameter – 5.06”

- Spindle taper – NMTB 40

- Spindle speed range RPM – 200-5000

- Spindle center to column face – 23”

- Spindle motor power – 7.5 HP

- Power requirement – 3 phase, 220V, 60 HZ; 37.5 FLA

- Power Requirement Control – 110V; 1 phase; 15A

- Maximum weight of workpiece – 2200 lbs.

- Height of table from bottom of bed – 38.25”

- Maximum spindle nose to table – 24”

- Minimum height – 95.5”

- Maximum height – 101”

- Width of machine including table – 110.5”

- Length with electric box door closed – 93.75”

- Overall width including full table travel – 171.65”

- Overall length with electrical door open – 119.5”

- Footprint – 42.52” x 63”

- Way surface – dovetail X axis; square ways Y and Z axis

- Weight (approximate) net – 7650 lbs.

- Weight (approximate) shipping – 7975 lbs.

- Maximum work capacities – Drilling (mild steel) max. dia. 1.00”; tapping, 5/8”; milling capacities, 7 inch3/min

- Way surfaces hardened and ground

- Turcite coating on all slide ways

- Automatic lubrication pump

- Auxiliary function hardware

- Limit switches

## Machine Options

- Glass scales for table and saddle

- Power drawbar

- Remote stop/go switch

- Coolant pump

- Spray coolant

- Table guard

- Halogen work lamp

- Chip pan / splash shield

- Vise

##### ProtoTRAK SMX System Specifications

(O) indicates optional feature

### ProtoTRAK System Hardware

- ProtoTRAK SMX CNC

- Two- or three-axis CNC, 3-axis DRO

- Real handwheels for manual operation

- 10.4” color active-matrix screen

- Industrial-grade Pentium® processor

- 1 GB Ram

- 4 USB connectors

- Override of program feedrate

- LED status lights built into display

- RJ45 Port and Ethernet card (O)

- Override of program spindle speed (O)

- USB Thumb drive flash memory 512 or more (O)

- Uncluttered front panel with few hard keys

- Ballscrew and motor assembly installed on quill

- Electronic quill handwheel

### Software Features – general operation

- Clear, uncluttered screen display

- Prompted data inputs

- English language – no codes

- Soft keys - change within context

- Windows® operating system

- Selectable two or three-axis CNC

- Color graphics with adjustable views

- Inch/mm selectable

- Convenient modes of operation

### DRO Mode features

- Incremental and absolute dimensions

- Jog at rapid with override

- Powerfeed X, Y or Z

- Do One CNC canned cycle

- Teach-in of manual moves

- Servo return to 0 absolute

- Tool offsets from library

- Go To Dimensions (O)

- Spindle speed setting with manual override (O)

- Fine/Course handwheel resolution

### Program Mode features

- Auto Geometry Engine (O)

- Geometry-based programming

- 3-axis geometry programming (O)

- Tool Path programming (O)

- Scaling of print data (O)

- Multiple fixture offsets (O)

- Programming of Auxiliary Functions

- Event Comments (O)

- Three-axis Geometry conversational programming (O)

- Incremental and absolute dimensions

- Automatic diameter cutter comp

- Circular interpolation

- Linear interpolation

- Look –graphics with a single button push

- List step – graphics with programmed events displayed

- Alphanumeric program names

- Program data editing

- Program pause

- Conrad – automatic corner radius

- Programmable spindle speeds

- Math helps with graphical interface

- Auto load of math solutions

- Tool step over adjustable for pocket routines

- Pocket bottom finish pass

- Selectable ramp or plunge cutter entry

- Subroutine repeat of programmed events

- Nesting

- Rotate about Z axis for skewing data

- Mirror of programmed events (O)

- Copy (O)

- Copy rotate (O)

- Copy mirror (O)

### Canned cycles

- Position

- Drill

- Bolt Hole

- Mill

- Arc

- Circle pocket

- Rectangular pocket

- Irregular Pocket (O)

- Circular profile

- Rectangular profile

- Irregular Profile(O)

- Circle Island (O)

- Rectangular Island (O)

- Irregular Island(O)

- Helix (O)

- Thread milling (O)

- Engrave(O)

- Tapping(O)

- Face Mill (O)

### Edit mode Features

- Delete events

- Erase program

- Spreadsheet editing (O)

- Global data change (O)

- G-Code editor (O)

- Clipboard to copy events between programs (O)

### Set Up Mode Features

- Program diagnostics

- Advanced tool library

- Tool names

- Tool length offset with modifiers

- Advanced diagnostic routines

- Software travel limits

- Tool path graphics with adjustable views

- Program run time estimation clock (O)

### Run Mode Features

- TRAKing

- Trial run at rapid

- 3D CAM file program run

- 3D G code file run with tool comp

- Real time run graphics with tool icon

- Countdown clock to next pause or tool change (O)

### Program In/Out Mode Features

- Program storage to USB Flash drive

- CAM program converter

- Converter for prior-generation ProtoTRAK programs

- DXF/DWG file converter (O)

- Selection of file storage locations (O)

- Automatic file back-up routine (O)

- Preview graphics for unopened files (O)

- Networking (O)

Control Options

### Advanced Features with Verify Option

- Verify – see a 3-D model machined before cutting chips

- Auto Geometry Engine ™

- Programmable Auxiliary functions

- 3-axis conversational programming

- Additional Canned Cycles:

- Irregular Pocket

- Circle Island

- Rectangular Island

- Irregular Island

- Irregular Profile

- Helix

- Thread milling

- Engrave

- Tapping

- Face Mill

- G-Code editor

- Countdown clock to next pause or tool change

- Total program time estimator

- Spreadsheet editing

- Global data change

- Scaling of print data

- Multiple fixture offsets

- Event comments

- Tool path conversational programming

- Mirror of programmed events

- Copy with or without offsets

- Copy Rotate

- Copy Mirror

- Clipboard to copy events between programs

### Networking Option

- Networking via RJ 45 port

### The DXF File Converter Option

- Import and convert CAD data into ProtoTRAK programs

- DXF or DWG files

- Chaining

- Automatic Gap Closing

- Layer control

- Easy, prompted process you can do right at the machine

### CAM Out Converter Option

- Save ProtoTRAK files as CAM files for running on different controls

### TRAKing/Electronic Handwheels Option

- Electronic Handwheels on X and Y (replaces the mechanical handwheels)

- TRAKing of programs during program run

- Go To Dimensions

- Selectable Fine/Coarse handwheel resolution