Southwestern Industries, Inc.
TRL 1440EX Lathe Specifications

with the ProtoTRAK EX Control

# Machine Specifications

- Height of Centers-7”

- Distance between centers-40”

- Swing over bed -14”

- Swing over saddle wings-14”

- Swing over cross slide-7.0”

- Cross slide travel-8.0”

- Tool section max-3/4”

- Coolant tank capacity - 3 gal.

- Width of Bed-8.1”

- Height of Bed-10.6”

- Spindle Nose (Camlock)-D1-4

- Spindle through hole-1.575”

- Spindle taper-MT#5

- Taper in reduction sleeve-3

- Spindle dia at front bearing-2.36”

- Number of bearings-2

- Spindle speed range (RPM)-60-2400

- Standard Tailstock Quill travel-5”

-	Quill diameter-1.575”                               Machine shown with optional features

-	Quill taper hole-MT#3

- Spindle Motor HP-5

- Power requirements, control-110V; 1P; 8A

- Power requirements, machine-220V;3P;60Hz

- Amps full load current-15

- Dimensions net - 73 x 44 x 57”

- Dimensions shipping - 78 x 49 x 67”

- Weight net – 1,800 lbs.

- Weight shipping – 2,250 lbs.

- Maximum rapid feed X - 100

- Maximum rapid feed Z - 100

- Coolant pump motor -1/8 HP

- Spindle motor brake - Magnetic

- Way surface hardness - 400 – 450 HB

- Head stock lubrication – Splash Lube

- Sliding door for easy set-ups

- Bedways hardened and ground

- Sliding surfaces Turcite coated

- Dovetails on cross slide, V-ways on saddle

- Adjustable saddle gibs

Machine Options

- Collet closer

- Chuck

- Coolant pump

- Face plate

- Follow rest

- Work lamp

- Remote stop/go switch

- Steady rest

- Tooling kit

##### ProtoTRAK ELX System Specifications

(O) indicates optional feature

### ProtoTRAK System Hardware

- ProtoTRAK ELX CNC

- Two-axis CNC, two-axis DRO

- Electronic handwheels for manual operation

- 7” color active-matrix screen

- Rugged industrial-grade processor

- 1 GB Ram

- 4 USB connectors

- Override of program feedrate

- Override of program spindle speed

- Gasket-sealed enclosures

- USB Thumb Drive Flash memory 512 or more (0)

- Clean front panel with few hard keys

### Software Features – General Operation

- Clear, uncluttered screen display

- Prompted data inputs

- English language – no codes

- Soft keys - change within context

- Windows® operating system

- Color graphics with adjustable views

- Inch/mm selectable

- Convenient modes of operation (see below)